M/V CAPTAIN BILL

SINGLE SCREW 2,000 H.P.

Length Overall………………	109 ft.

Beam…………………………	29 ft.

Depth………………………...	16 ft.

Maximum Draft…………….	15 ft.

CAPACITIES						ELECTRONICS

Fuel Oil			28,600	gal.			Radars			Furuno 48nm

Ballast			10,000 	gal.						JRC 36 nm

Potable Water		1,200	gal.			Radios			(2) Standard VHF

Lube Oil		710	gal.			Chart plotter		Garmin 2010C

AIS			JRC

MACHINERY						Fathometer		Navman

Hailer			Standard

Main Engine		Fairbanks Morse

10-38D 8 1/8			ACCOMADATIONS

Horsepower		2,000

Reduction Gear		Western 5.95:1 ratio		Staterooms		(2) 2-man (2) 4-man

Generators		(2) 60KW 208V			Heads			1

Driven By		(2) 6-71 Detroit Diesel		Galley Seating		6 men

Propeller		144”x 112” 4 Blade SS		Heat			electric/oil fired

PERFORMANCE					FIREFIGHTING

Speed Light Tug						-(2) Fire Monitors driven by 6-71 with Goulds

Maximum		12 kts. @ 850 RPM		 pump rated @ 2,000 GPM

Cruising		9.5 kts. @ 700 RPM		-1,500 gal. foam capacity with booster pump

REGISTRATION					OTHER EQUIPMENT

Flag			United States			-Electric/Hydraulic stern capstan 10,000 lb. pull

Home Port		Wilmington, DE.		-150 lb. semi-portable CO2 system in machinery

Official Number		1109004				 space with 50’ hose reel

Builder			Marinette Marine

Year Built		1967

Tonnage		235 GRT   70 NRT		revised  4-09